Standard Operating Procedures

Location:________________________ P.I.______________________ Date:__________

Section 1.  Hazard Class- Organic Acids

Section 2.  Describe Hazard Class- Concentrated organic acid solutions.  Examples are acetic and formic acids

Section 3.  Potential Hazards- Corrosive material. Liquid and mist can cause severe burns to all body tissues.  Inhalation of vapor is harmful, could damage lungs. Ingestion may be fatal. Liquid can cause severe damage to skin and eyes.  Flammable liquid and vapor.

Section 4.  Personal Protective Equipment- When working with small amounts use chemical safety glasses and butyl or neoprene gloves.  Must have proper exhaust ventilation in room or use a fume hood.  When pouring large amounts, use safety goggles a face shield, and a chemical resistant apron.

Section 5.  Engineering Controls- When possible, dispense chemical under a fume hood.  The room where the chemical is being used should be equipped with proper exhaust ventilation to keep the airborne concentration below the allowable exposure limit.  Eye wash station and a safety shower must be accessible within a 10 second travel time and not require passage through more than one door.

Section 6.  Special Handling and Storage Requirements- Store in a cool, dry, ventilated area, away from spark or flame, with other compatible substances.  Keep away from strong bases, oxidizers, cyanides, inorganic materials and metals such as zinc and mercury.  Do not store in metal containers.  When diluting, always add the acid into water slowly with stirring, never the other way around.  Containers should be bonded and grounded for transfers to avoid static sparks.  Containers of this product are hazardous when empty until neutralized with a mild Sodium Bicarbonate solution.

Section 7. Spill and Accident Procedures-

Inhalation: Remove to fresh air.  If not breathing, give artificial respiration.  Get medical attention immediately.

Ingestion: DO NOT INDUCE VOMITING.  Give large quantities of water or milk.  Never give anything by mouth to an unconscious person.  Get medical attention immediately.  Poison control number is: 1-800-222-1222

Skin Contact: Immediately flush skin with copious amounts of water for at least 15 minutes while removing any contaminated clothing.  Get medical attention immediately.

Eye Contact: Immediately flush eyes with copious amounts of water for at least 15 minutes.  Get medical attention immediately.

Small Spills (One Liter or less): Ventilate the area and use proper personal protective equipment.  Neutralize with alkaline material such as Soda Ash or Sodium Bicarbonate.  Absorb the material with an inert absorbent such as vermiculite or sand and place in a suitable container labeled with the words “hazardous waste” and its constituents, and notify EH&S for pickup.

Large Spills (More than a Liter): Notify those affected by the spill and turn off all ignition sources.  Evacuate the area and call Environmental Health and Safety at 297-3129 or campus police at 297-3500.  Restrict people from entering the affected area until cleanup is completed.

Section 8. Decontamination Procedures- To decontaminate, wipe areas with a mild solution of Sodium Bicarbonate.  Place all material in a proper container, labeled “hazardous waste” and its constituents, and notify EH&S for pickup.

Section 9. Waste Disposal Procedures- Place waste in an appropriate and compatible container.  Container must be closed and labeled with the main constituents and the words “hazardous waste.”  Place waste in waste collection area and call EH&S at 297-3129.

Section 10. Material Safety Data Sheets Locations- Material Safety Data Sheets are kept in a binder labeled MSDS in room___, or may be found on the web at either www.siri.org or www.fau.edu/ehs.

Section 11. Principal Investigator/ Lab Manager Approval:

Signature: ___________________________________

Date: _______________________________________