Standard Operating Procedure

Location:________________________ P.I.______________________ Date:__________

Section 1.  Hazard Class- Flammables

Section 2.  Describe Hazard Class- Flammable liquids such as Acetone, Methanol, Ethanol, Ethers, etc.

Section 3.  Potential Hazards- Extremely Flammable Liquid:  May cause respiratory tract irritation.  May cause central nervous system depression.  May cause liver and kidney damage.  Causes eye and skin irritation. Target organs of most concern are Kidneys, central nervous system, liver, respiratory system, eyes, and skin.

Section 4.  Personal Protective Equipment- When working with small amounts wear a lab coat and use chemical safety glasses with side shields and PVC or neoprene gloves.  Must have proper exhaust ventilation in room or use a fume hood.  When pouring large amounts, use safety goggles a face shield, and a chemical resistant apron

Section 5.  Engineering Controls- Use the protective safety equipment as listed in section 4.  The room where the flammable liquid is stored should be equipped with proper exhaust ventilation to keep the airborne concentrations below the allowable exposure limits.  Eye wash station and a safety shower must be accessible within a 10 second travel time and not require passage through more than one door.

Section 6.  Special Handling and Storage Requirements- Flammable liquids should be stored in a cool and dry room with proper ventilation.  Flammable liquids should be stored in closed containers with tight fitting lids.  Keep away from any sources of ignition.  Flammable liquids in excess of 10 gallons are to be stored in an approved  Flammable Storage Cabinet.

Section 7. Spill and Accident Procedures-

Inhalation: Remove to fresh air.  If not breathing, give artificial respiration.  Get medical attention immediately.

Ingestion: Give large quantities of water.  Never give anything by mouth to an unconscious person.  Get medical attention immediately.  Poison Control number: 1-800-222-1222

Skin Contact: Immediately flush skin with copious amounts of water for at least 15 minutes while removing any contaminated clothing.  Get medical attention immediately.

Eye Contact: Immediately flush eyes with copious amounts of water for at least 15 minutes.  Get medical attention immediately.

Small Spills (One Liter or less): Ventilate the area and use proper personal protective equipment.  Absorb the material with an inert absorbent such as vermiculite or sand and place in a suitable container, labeled with the words “hazardous waste” and the main constituents, and notify EH&S for pickup.

Large Spills (More than a Liter): Notify those affected by the spill, evacuate the area, turn off all ignition sources and call Environmental Health and Safety at 297-3129 or campus police at 297-3500.  Restrict people from entering the affected area until cleanup is completed.

Section 8. Decontamination Procedures- To decontaminate, wipe areas with a solution of 2-5% Soda Ash.  Place all material in a container labeled with the words  “Hazardous Waste” and the contents, and notify EH&S for pickup.

Section 9. Waste Disposal Procedures- Place waste in an appropriate and compatible container.  Container must be closed and labeled with the words “Hazardous Waste” and with the main constituents.  Place waste in waste collection area and call EH&S at 297-3129.

Section 10. Material Safety Data Sheets Locations- Material Safety Data Sheets are kept in a binder labeled MSDS in room___, or may be found on the web at either www.siri.org or www.fau.edu/ehs.

Section 11. Principal Investigator/ Lab Manager Approval:

Signature: ___________________________________

Date: _______________________________________