Standard Operating Procedures

Location:________________________ P.I.______________________ Date:__________

Section 1.  Hazardous Chemical- Formaldehyde

Section 2.  Describe Hazardous Chemical- Use of Formaldehyde (37%) or Formalin.

Section 3.  Potential Hazards- Harmful if inhaled or absorbed through skin.  May be fatal or cause blindness if swallowed.  Causes irritation to skin, eyes and respiratory tract.  May cause cancer.  Cancer risk depends on level and duration of exposure.  Strong sensitizer. The perception of formaldehyde by odor and eye irritation becomes less sensitive with time as one adapts to formaldehyde. This can lead to overexposure if a worker is relying on formaldehyde's warning properties to alert him or her to the potential for exposure.

Section 4.  Personal Protective Equipment- When working with formaldehyde use chemical safety glasses and butyl or nitrile gloves.  Wear a lab coat or a chemical apron.  If dispensing large amounts, wear goggles and a face shield.  Must have proper exhaust ventilation in room or use a fume hood.  If airborne exposures are suspected, contact EH&S at 7-3129 for consultation.

Section 5.  Engineering Controls- When possible, dispense chemical under a fume hood.  The room where the chemical is being used should be equipped with proper exhaust ventilation to keep the airborne concentration below the allowable exposure limit.  If airborne exposures are suspected, contact EH&S at 7-3129 for consultation.  Eye wash station and a safety shower must be accessible within a 10 second travel time and not require passage through more than one door.

Section 6.  Special Handling and Storage Requirements- Store in a cool, dry, ventilated area with other compatible substances.  Keep away from flammables and oxidizers.  Avoid static sparks.  Protect from freezing.  Containers of this product are hazardous when empty until neutralized with a mild Sodium Bicarbonate solution.  The rinse solution must be collected and managed as hazardous waste.

Section 7. Spill and Accident Procedures-

Inhalation: Remove to fresh air.  If not breathing, give artificial respiration.  Get medical attention immediately.

Ingestion: Give large quantities of water or milk.  If vomiting occurs, keep head lower than hips.  Never give anything by mouth to an unconscious person.  Get medical attention immediately.  Poison Control number: 1-800-222-1222

Skin Contact: Immediately flush skin with copious amounts of water for at least 15 minutes while removing any contaminated clothing.  Get medical attention immediately.

Eye Contact: Immediately flush eyes with copious amounts of water for at least 15 minutes.  Get medical attention immediately.

Small Spills (One Liter or less when in solution): Do not attempt cleanup if you feel unsure of your ability to do so, or if you perceive the risk to be greater than normal laboratory operations. Ventilate the area and use proper personal protective equipment.  Absorb the material with an inert absorbent such as vermiculite or sand and place in a suitable container, label with the words “hazardous waste” and the constituents and notify EH&S for pickup.

Large Spills (More than a Liter): Notify those affected by the spill and turn off all ignition sources.  Evacuate the area and call Environmental Health and Safety at 297-3129 or campus police at 297-3500.  Restrict people from entering the affected area until cleanup is completed.

Section 8. Decontamination Procedures- To decontaminate, wipe areas with a mild solution of Sodium Bicarbonate.  Place all material in a proper container labeled “hazardous waste” and notify EH&S for pickup.

Section 9. Waste Disposal Procedures- Place waste in an appropriate and compatible container.  Container must be closed and labeled “hazardous waste” along with the main constituents.  Place waste in waste collection area and call EH&S at 297-3129.

Section 10. Material Safety Data Sheets Locations- Material Safety Data Sheets are kept in a binder labeled MSDS in room___, or may be found on the web at either www.siri.org or www.fau.edu/ehs.

Section 11. Principal Investigator/ Lab Manager Approval:

Signature: ___________________________________

Date: _______________________________________