Standard Operating Procedures

Location:________________________ P.I.______________________ Date:__________

Section 1.  Hazardous Chemical- Hydrogen Peroxide 30-50%

Section 2.  Describe Hazardous Chemical- Use of concentrated solutions of Hydrogen Peroxide

Section 3.  Potential Hazards- Extremely hazardous material.  Strong Oxidizer.  Corrosive.  Contact with organic material may start a fire.  Harmful if inhaled or absorbed through skin, could cause burns.  May be fatal or cause blood abnormalities if swallowed.  Causes irritation to skin, eyes and respiratory tract.  Can cause permanent eye damage.

Section 4.  Personal Protective Equipment- When working with hydrogen peroxide use chemical safety glasses with side shields and butyl, nitrile or viton gloves.  Wear a lab coat or a chemical apron.  If dispensing large amounts, wear a rubber, neoprene or PVC apron, goggles and a face shield.  Must have proper exhaust ventilation in room or use a fume hood.

Section 5.  Engineering Controls- When possible, dispense chemical in a fume hood.  The room where the chemical is being used should be equipped with proper exhaust ventilation to keep the airborne concentration below the allowable exposure limit.  If airborne exposures are suspected, contact EH&S at 7-3129 for consultation.  Eye wash station and a safety shower must be accessible within a 10 second travel time and not require passage through more than one door.

Section 6.  Special Handling and Storage Requirements- Store in a cool, dry, ventilated area with other compatible substances.  Keep away from organic material, flammable vapors, oxidizers, organic materials, strong bases, reducing agents, powdered metals, metallic salts and alkalizes.  Do not store directly on wooden shelves, store in a plastic tub for secondary containment.  Inspect periodically for bulging containers.

Section 7. Spill and Accident Procedures-

Inhalation: Remove to fresh air.  If not breathing, do not give artificial respiration by mouth, use oxygen bag.  Get medical attention immediately.

Ingestion: DO NOT INDUCE VOMITING.  Give large quantities of water or milk.  Never give anything by mouth to an unconscious person.  Get medical attention immediately.  Poison Control number: 1-800-222-1222

Skin Contact: Immediately flush skin with copious amounts of water for at least 15 minutes while removing any contaminated clothing.  Get medical attention immediately.

Eye Contact: Immediately flush eyes with copious amounts of water for at least 30 minutes.  Get medical attention immediately.

Small Spills (One Liter or less when in solution): Ventilate the area and use proper personal protective equipment.  Absorb the material with an inert absorbent such as vermiculite or sand, do not use paper towels or other oxidizable materials! Place all materials in a suitable container for disposal, label with the words “hazardous waste” and the contents and notify EH&S for pickup.

Large Spills (More than a Liter): Notify those affected by the spill and turn off all ignition sources.  Evacuate the area and call Environmental Health and Safety at 297-3129 or campus police at 297-3500.  Restrict people from entering the affected area until cleanup is completed.

Section 8. Decontamination Procedures-  May be neutralized with sodium metabisulfite or sodium sulfite after diluting to 5-10% peroxide. Place all material in a proper container labeled “hazardous waste” and its constituents, and notify EH&S for pickup.

Section 9. Waste Disposal Procedures- Place waste in an appropriate and compatible container.  Container must be closed and labeled with the main constituents and the words “hazardous waste.”  Place waste in waste collection area and call EH&S at 297-3129.

Section 10. Material Safety Data Sheets Locations- Material Safety Data Sheets are kept in a binder labeled MSDS in room___, or may be found on the web at either www.siri.org or www.fau.edu/ehs.

Section 11. Principal Investigator/ Lab Manager Approval:

Signature: ___________________________________

Date: _______________________________________