Standard Operating Procedures

Location:________________________ P.I.______________________ Date:__________

Section 1.  Hazardous Chemical- Phenol

Section 2.  Describe Hazardous Chemical- Laboratory use of Phenol

Section 3.  Potential Hazards- POISON- May be fatal if inhaled, swallowed or absorbed through skin.  Rapidly absorbed through skin.  Causes severe burns to body parts upon contact.  Corrosive.  Combustible liquid and vapors.

Section 4.  Personal Protective Equipment- When working with phenol use chemical safety glasses and viton or neoprene gloves.  Wear a lab coat or a chemical apron.  If dispensing large amounts, wear goggles and a face shield.  Must have proper exhaust ventilation in room or use a fume hood.

Section 5.  Engineering Controls- When possible, dispense chemical under a fume hood.  The room where the chemical is being used should be equipped with proper exhaust ventilation to keep the airborne concentration below the allowable exposure limit.  If airborne exposures are suspected, contact EH&S at 7-3129 for consultation.  Eye wash station and a safety shower must be accessible within a 10 second travel time and not to require passage through more than one door.

Section 6.  Special Handling and Storage Requirements- Store in a cool, dry, ventilated area with other compatible substances.  Keep away from flammable vapors, oxidizers and control ignition sources.  Containers of this product are hazardous when empty.  Empty containers should be placed in satellite accumulation area for disposal by EH&S.

Section 7. Spill and Accident Procedures-

Inhalation: Remove to fresh air.  If not breathing, give artificial respiration.  Get medical attention immediately.

Ingestion: Immediately administer castor oil or vegetable oil (15-30 cc).  Never give anything by mouth to an unconscious person.  Get medical attention immediately.  Poison Control number: 1-800-222-1222.

Skin Contact: Immediately flush skin with copious amounts of water for at least 30 minutes while removing any contaminated clothing.  Apply Polyethylene Glycol to the affected area.  Get medical attention immediately.

Eye Contact: Immediately flush eyes with copious amounts of water for at least 15 minutes.  Get medical attention immediately.

Small Spills (One Liter or less when in solution): Ventilate the area and use proper personal protective equipment.  Absorb the material with an inert absorbent such as vermiculite or sand and place in a suitable container labeled with the words “hazardous waste” and its constituents, and notify EH&S for pickup.

Large Spills (More than a Liter): Notify those affected by the spill and turn off all ignition sources.  Evacuate the area and call Environmental Health and Safety at 297-3129 or campus police at 297-3500.  Restrict people from entering the affected area until cleanup is completed.

Section 8. Decontamination Procedures- Dry lime or Soda Ash may be used to neutralize the material.  Place all material in a proper container, label with the words “hazardous waste” and its constituents, and notify EH&S for pickup.

Section 9. Waste Disposal Procedures- Place waste in an appropriate and compatible container.  Container must be closed and labeled with the main constituents and the words “hazardous waste”.  Place waste in waste collection area and call EH&S at 297-3129.

Section 10. Material Safety Data Sheets Locations- Material Safety Data Sheets are kept in a binder labeled MSDS in room___, or may be found on the web at either www.siri.org or www.fau.edu/ehs.

Section 11. Principal Investigator/ Lab Manager Approval:

Signature: ___________________________________

Date: _______________________________________